## Slide 1: Vehicle Blind Spot Assist System
Tanzim Mokammel
Valikhan Kuparov
Hani Hadidi

## Slide 2: Motivation
Introduce an universal system that can potentially be used on real cars to reduce accidents related to lane changing
Experiment with vehicle automation features in order to contribute to advancing accident prevention technologies

## Slide 3: Project Goal
Design a system that will detect obstacles present or approaching a remote-controlled vehicle’s blind spot
Attain control of the remote-controlled vehicle to prevent user’s from steering into an obstacle

## Slide 4: System Level Overview

## Slide 5: Module Level Descriptions – Obstacle Detection/Anticipation

## Slide 6: Module Level Descriptions – User Feedback

## Slide 7: Module Level Descriptions – Automation

## Slide 8
Alternatives
Input
Output
Controller
Automation

## Slide 9: Alternatives - Input
Input - Obstacle Detection | SRF05 Ultrasonic Rangefinder | Good range (~ 3m) and accuracy (± 2% error), relatively cheap ($40) | Complex programming required; relatively expensive; prone to interference from miscellaneous obstacles
 | LR3 - Precision USB Laser Rangefinder | Very high accuracy (±3mm) and range (30m) | Expensive ($150); requires external tools, very sensitive to light conditions
 | Sharp IR Rangefinder R48-IR12 | Very cheap ($15); immune to ambient light interference; low power consumption | Narrow beam width; prone to other IR sensor interference, low range (10 cm - 80 cm)
 | Camera - image detection | Accurate; images can be reproduced for the driver | Complex image processing algorithms required; expensive

## Slide 10: Alternatives - Output
Output - Feedback | Visual | Very informative; aesthetically pleasing | Distracting; expensive; may experience scaling issues, resulting in inaccurate and unreliable output
 | Numerical | Quantitative; very accurate; informative | May cause confusion among some users; aesthetically displeasing
 | Simple - blinking light | Inexpensive; Easy to implement; very simple, yet informative | No quantitative feedback; small in size
 | Auditory - Beeping sounds | Easy to implement; Inexpensive; simple | Irritating; may be inaudible due to music or ambient sounds
 | Physical - Vibration of the steering wheel | Very effective | Distracting; vehicle dependent

## Slide 11: Alternatives - Microcontroller
Component | Possible solution | Advantages | Disadvantages
Micro-Controller | Arduino Uno | Programmed using C/C++; cheap ($30); Easy to use due to its IO pins | Relatively bigger in size than other controllers
 | Picaxe | Comes with software that allows flow charts; No programming required; Easy to work with | Limited functionality

## Slide 12: Alternatives - Automation
Automation | Automated Lane Merging System | Allows the user to easily and safely change lanes | The automated lane change system may cause the undesirable vehicle speeds; the automated system may not be able to change lanes fast enough for certain cases such as exiting the freeway; impractical during high traffic
 | Steering-Lock | Prevents collisions during lane changes | Takes away the user’s judgment factor; may cause a more serious frontal collision

## Slide 13: Validation Tests
Requirements |  | Test | Acceptance Criteria
Obstacle detection/anticipation | Sensors should measure distances accurately | Place obstacles at 4 different distances(3cm, 1m, 2m, 3m) away from the sensors | Computed distances match the measured distances within ±2.5% error
 | Blind spot Coverage | Mount the sensors on the remote controlled (RC) car to cover the defined blind spot (Appendix F); place obstacles within it | The sensors detect the presence of the obstacle within the defined range
 | Microcontroller should compute relative speed based on distance values | Mount sensors to the RC car; place an obstacle and the RC car in motion with a known relative speed | The microcontroller’s calculated speed values match the known value within ±5% error
 | Obstacle Anticipation | Set up situations where both distance and relative speeds are known, and perform allowed time calculations with the microcontroller | The microcontroller’s time values match the calculated ones within ±12% error
Output | The Light Emitting Diodes (LED) and the display should provide accurate feedback to the user | Observe the feedback response of the LED and the Liquid Crystal Display (LCD) display | The LED should behave according to the defined look-up table (Appendix H); the display should contain calculated values of distance to obstacle; relative speed, and time left for a lane change
Auto- Mation | The steering of the RC car should lock when necessary | Simulate the extremely dangerous, and very unsafe cases (Appendix H) | The steering of the user car is irresponsive in the direction of the obstacle

## Slide 14: Gantt Chart

## Slide 15: Deliverables for December Review
Distance/Speed Calculations
LED/LCD Display Implementations
Integration of Sensors with Output
Control of a RC Car

## Slide 16: Overall Technical Roles
Tanzim
  Sensor Programming (acquiring distance, and relative speed)
Valikhan
  Output Module Programming (LED, Display), and integration with sensors
Hani
  Control of RC Vehicle through the microcontroller